## Slide 1: Dynamic Causal Modelling

## Slide 2: State Space Model (SSM) popular as Dynamic Causal Model (DCM)
Valdes-Sosa, P. A., Sanchez-Bornot, J. M., Sotero, R. C., Iturria-Medina, Y., Aleman-Gomez, Y., Bosch-Bayard, J., Carbonell, F., & Ozaki, T. (2009). Model driven EEG/fMRI fusion of brain oscillations. Human Brain Mapping, 30(9), 2701–2721. https://doi.org/10.1002/hbm.20704
For EEG-fMRI

## Slide 3: DCM Framework
Stimulus from Buchel and Friston, 1997
Figure 3 from Friston et al., Neuroimage, 2003
Brain by Dierk Schaefer, Flickr, CC 2.0
Experimental Stimulus (u)
Observations (y)
z = f(z,u,θn)
.
How brain activity z changes over time
y = g(z, θh)
What we would see in the scanner, y, given the neural model?
Neural Model
Observation Model

## Slide 4: DCM Framework
Experimental Stimulus (u)
Observations (y)
Neural Model
Observation Model
Model Inversion
(Variational Laplace)
Given our observations y, and stimuli u, what parameters θ make the model best fit the data?

## Slide 5: Single Source Model for EEG/MEG
David, O., Kiebel, S. J., Harrison, L. M., Mattout, J., Kilner, J. M., & Friston, K. J. (2006). Dynamic causal modeling of evoked responses in EEG and MEG. NeuroImage, 30(4), 1255–1272. https://doi.org/10.1016/j.neuroimage.2005.10.045

## Slide 6: Sample Task
Mismatch Negativity (MMN)
Garrido, M. I., Kilner, J. M., Kiebel, S. J., Stephan, K. E., & Friston, K. J. (2007). Dynamic causal modelling of evoked potentials: A reproducibility study. NeuroImage, 36(3), 571–580. https://doi.org/10.1016/j.neuroimage.2007.03.014
Standard Stimulus
1000 Hz
80% (480) trials
Rare Stimulus
2000 Hz
20% (120) trials
70 ms
5 ms rise and fall time
70 ms
5 ms rise and fall time

## Slide 7: Recorded EEG signal analysis
5s epoched from − 100 to 400 ms after the stumulus onset
Bandpass filtered [0.5, 40] Hz
re-referenced to the average of the right and left ear lobes
DCM
down-sampled to 200 Hz
Garrido, M. I., Kilner, J. M., Kiebel, S. J., Stephan, K. E., & Friston, K. J. (2007). Dynamic causal modelling of evoked potentials: A reproducibility study. NeuroImage, 36(3), 571–580. https://doi.org/10.1016/j.neuroimage.2007.03.014

## Slide 8: DCM space model
Garrido, M. I., Kilner, J. M., Kiebel, S. J., Stephan, K. E., & Friston, K. J. (2007). Dynamic causal modelling of evoked potentials: A reproducibility study. NeuroImage, 36(3), 571–580. https://doi.org/10.1016/j.neuroimage.2007.03.014

## Slide 9: DCM analysed data
In SPM website
  https://www.fil.ion.ucl.ac.uk/spm/data/eeg_mmn/

## Slide 10: Exercise
Download, unzip and add spm12 to Matlab
  Use Set Path, Add Folder

## Slide 11: Exercise
Type “spm eeg” in Matlab command line
Click on DCM

## Slide 12: Exercise
Click on Load and open “DCM_subject1.mat”
Select “ERPs (sources)”
1
2

## Slide 13: Population Activities

## Slide 14: Exercise
Select “Scalp maps”
1

## Slide 15: Scalp Maps (standard and rare conditions)